## Slide 1
Molecular Simulation using Machine Learning Interatomic Potentials
EXPLORING THE DEEPMD-KIT FRAMEWORK | Bachelor Thesis Project (JULY - NOV 2025)
Student: Vanshita Bihani (Roll No. 220107093)
Supervisor: Prof. Amit Kumar
Department of Chemical Engineering, IIT Guwahati

## Slide 2
Domain: Molecular Dynamics (MD) simulations for predicting material properties at the atomic scale.
Current Challenge: The trade-off between efficiency and accuracy.
Scope: Validate Deep Potential (MLIP) to bridge this gap, using Methane (CH4) as a case study for stiff bonds and weak dispersion.
Classical Force Fields are fast but chemically inaccurate.
Ab Initio MD (AIMD) is accurate but computationally prohibitive (O(N^3)).
Problem Statement

## Slide 3
Current Practice
Researchers rely on Classical Force Fields (AMBER/CHARMM) for large systems or AIMD for small, reactive clusters. Neither scales well for accurate transport properties.
Why Insufficient?
Classical models cannot capture bond breaking or polarization. AIMD is limited to picoseconds, failing to capture diffusion and thermal conductivity in bulk liquids.
The Use Case
Methane (CH4) is challenging: it has stiff intramolecular covalent bonds requiring quantum accuracy, but interacts inter-molecularly via weak Van der Waals forces.
Background & Motivation

## Slide 4
Theoretical Foundation: Review the evolution from empirical Force Fields to Neural Network Potentials.
Implementation: Establish a "Data-to-Discovery" pipeline using DeepMD-kit for training and LAMMPS for simulation.
Validation: Assess the model's accuracy on Methane's structural (bond length) and transport properties (Diffusion, Conductivity).
Primary Objective: Demonstrate that Deep Potential can bridge the gap between quantum accuracy and classical efficiency for complex fluids.
Project Objectives

## Slide 5
Evolution of Potentials
•
Classical (AMBER/CHARMM): Efficient (O(N)), but rigid and non-reactive.
•
Reactive (ReaxFF): Handles chemistry, but requires complex parameter fitting.
•
Neural Networks (BPNN/DP): Learn the Potential Energy Surface directly from quantum data.
Selection: We chose DeepPot-SE (Deep Potential Smooth Edition) because it offers the optimal balance of accuracy and inference speed required for nanosecond-scale transport simulations.
Literature Review: Existing Approaches

## Slide 6
1. Data Acquisition
Collect high-fidelity Ab Initio (DFT) data for atomic configurations (Energies & Forces).
2. Model Training
Train DeepPot-SE model using DeepMD-kit to map descriptors to potential energy.
3. Compression
Compress the trained model graph to accelerate inference speed for MD.
4. MD Simulation
Run large-scale simulations in LAMMPS to calculate transport properties.
Methodology: Overall Workflow

## Slide 7
DeepPot-SE Architecture
The model uses an Embedding Network to transform local atomic environments into symmetry-invariant descriptors. A Fitting Network (ResNet) then maps these descriptors to atomic energies. This ensures the potential is smooth and continuous.
Simulation Setup
Integrator: Velocity Verlet with 0.1 fs timestep (for fast C-H vibrations).
Diffusion: Calculated via Einstein Relation (Mean Square Displacement).
Conductivity: Calculated via Green-Kubo relations (Heat Flux Autocorrelation).
Methodology Details

## Slide 8
Model Accuracy
Microscopic Structure
The Radial Distribution Function (RDF) shows a sharp peak at 1.1 Å, matching the experimental C-H bond length of 1.09 Å. The model learned the "stiff spring" nature of the bond without explicit harmonic parameters.
Energy RMSE: 0.92 meV/atom (Chemical accuracy).
Force RMSE: 121 meV/Å (Sufficient for dynamics).
Results: Structural Validation (Case Study)

## Slide 9
Macroscopic Agreement
Self-Diffusion Coefficient (D):
~2.3 nm^2/s
This is remarkably close to the experimental value of 2.6 nm^2/s.
Key Insight
The Deep Potential model successfully captured weak intermolecular dispersion forces in the dense liquid phase, a property usually requiring complex Lennard-Jones tuning, while maintaining quantum accuracy.
Results: Transport Properties & Insights (Case Study)

## Slide 10
Conclusions
Future Work (BTP-II)
•
Successfully established a data-to-discovery pipeline using DeepMD-kit.
•
Validated the model on Methane, reproducing both microscopic bond lengths and macroscopic transport coefficients.
•
Demonstrated that MLIPs can achieve "AIMD-quality" results at nanosecond timescales.
•
Active Learning: Implement the DP-GEN loop to automate data exploration.
•
Complex Systems: Extend simulations to natural gas mixtures (CH4/C2H6) or interfaces.
•
Reactivity: Attempt high-temperature combustion simulations to test bond breaking.
Conclusions & Future Work

## Slide 11
Thank You 